## Slide 1: Introducing FGT600D

## Slide 2: FortiGate 600D
2x GE RJ45 Management Ports
8x GE SFP Slots
8x GE RJ45 Ports
2x 10GE SPF+ Slots
Hardware Performance |  |  | 
Firewall Throughput (1518/512/64) | 36/36/24Gbps | IPS Throughput | 7 Gbps
Firewall Latency | 3 μs | Antivirus Throughput (Proxy Based) | 3 Gbps
Concurrent Sessions | 5.5 Mil | Virtual Domains (Default / Max) | 10/10
New Sessions/Sec | 270,000 | Max Number of FortiAPs (Total/Tunnel) | 1024 / 512
Firewall Policies | 10,000 | Max Number of FortiTokens | 1,000
IPSec VPN Throughput | 20 Gbps | Client-to-Gateway IPSec VPN Tunnels | 10,000
SSL-VPN Throughput | 2.2 Gbps | Concurrent SSL-VPN Users (Recommended Max) | 5,000
1
2
3
4
1
2
3
4

## Slide 3: FortiGate 600D Schematic
RAM
8GB
Intel Core i7
1G
1G
Ser
Console
2 x 1G Management
STORAGE
120GB
SFP
SFP
1G
SFP
1G
1G
8x GE RJ45
USB
USB
CP8
CP8
Flash
16 GB
USB
Quad Core
CPU
RJ45
RJ45
1G
RJ45
1G
1G
8 x GE SFP
SFP
1G
…
…
RJ45
1G
2x 10G
SFP/SFP+
10G
10G
10G
10G
AC PSU
External RPS Connector
FRPS-100
NP6
Notes: 3